1.3 ANSWER

In order to provide the pair of trackers on the required timescale it is essential that the technology choice be made at the October 2003 MICE collaboration meeting. MICE has therefore asker two senior physicists (G. Gregoire and D. Summers) to specify the criteria on which the decision is to be made and to oversee the decision-making process.

The most important issue common to both tracker options is the sensitivity of the device to background X-rays generated by the RF cavities. Exposures of samples of scintillating fibre to the radiation produced by an 805 MHz cavity have been performed and will continue. A prototype TPG will be exposed to x-rays, and possibly to the same cavity so that the background rate can be determined (see section 1.2).

The following paragraphs summarise the plans to address the technology-specific issues in time for the tracker decision point in October.

1.3.1 The scintillating fiber tracker

The key factors that need to be addressed for the scintillating-fibre tracker are:

Precision of fabrication: the fibre planes must be held precisely and be stable to high precision;

Light yield: the light yield at the VLPC (i.e. including any losses in all optical connectors) must be shown to be sufficient to allow the electronic noise to be removed while maintaining high efficiency for minimum-ionising particles;

Cross-talk: the small fibre-diameter gives rise to the possibility of cross talk between neighbouring fibres. The level of cross talk must be measured and be shown to be acceptably small;

Multiplexing scheme: the proposed multiplexing scheme must be demonstrated.

In order to address these issues the scintillating fibre group is planning to build a single-station prototype and to operate it in the D0 cosmic ray test stand in September 2003. Construction of the prototype will allow the precision of the fabrication to be demonstrated. Measurements in the D0 test stand will determine the light yield and cross talk. The multiplexing scheme will also be demonstrated in this test.

1.3.2. The TPC+GEM tracker

The TPC's operate on well known principles and are very tempting as nearly massless  tracking device. The original idea here is to replace the usual "MWPC" planes near the anode with a stack of 3 GEM foils. But the dominant problems of  TPCs (S/N ratio, crosstalk ...) are exacerbated here in a situation where intense RF fields are present.

The criterions to be are as follows (see also section 1.2)

- Understanding of the performance and resolution of the TPG. The milestone to be passed are the observation of tracks in a prototype TPC in the former Aleph-Harp magnet.  The same stand should be used to check the basic parameters of operation of a TPC+GEM setup with a 55Mn x-ray source: measurements of the x-ray energy, mean free path of electrons and photons, track reconstruction, calibration ..

- The calibration strategy and sensitivity of the TPG to possible field inhomogeneities should be addressed.

- The operability of the chamber in an intense flux of x-rays should be demonstrated by exposing a TPC with GEMs to a known source. This can be done by exposing a TPG to radioactive sources, but preferably the tests should be performed in a situation similar to the lab G test stand.

- The performance of the reconstruction in presence of several simulataneous tracks, x-ray background and inefficiencies should be simulated.

The results should be presented at the collaboration in october 2003.